## Slide 1
Istanbul Metrobus
Analytical Station-Slot Control System
52 km Corridor
45 Stations
Real-Time Simulation
SmartStop · HeadwayModel · StopInterface · ControlMerger
1 / 10

## Slide 2
Problem Statement & Objectives
2 / 10
The Problem
• Bus bunching: vehicles cluster, leaving large gaps
• 800,000+ daily passengers on 52 km corridor
• Traditional headway control treats the symptom,
• not the root cause
• Station platform overflow cascades through the fleet
Objectives
• Prevent station slot overflow
• Minimize queue cascade effects
• Real-time speed recommendations (10 FPS)
• Analytical solution — no ML required
• O(S x 2) complexity per tick

## Slide 3
Background & Motivation
3 / 10
52 km
Corridor Length (Beylikduzu - Sogutlucesme)
45
Stations on Route
800K+
Daily Passengers
~2 min
Target Headway (rush hour)
Why Slot-Based Control?
Headway control
fixes gaps reactively — after bunching occurs
Slot control
prevents overflow proactively — before bunching starts
Each stop
independently manages its zone (1-2 vehicles) — O(1) per stop
Cascade effect
one overflowed stop delays all following vehicles

## Slide 4
Design Methodology
4 / 10
Physics Engine 20 Hz
>
SmartStop x45 Zone Mgr
>
StopInterface Coordination Pub/Sub
>
ControlMerger Command Output
>
Dashboard 10 FPS WebSocket
Design Principles
Purely Analytical
No ML, no RL — deterministic formulas only
Decentralized
Each SmartStop manages only its zone (~1-2 vehicles)
Single Thread
asyncio cooperative multitasking — no locks, no races
Forward Safety
Collision prevention layer — cannot be overridden

## Slide 5
Implementation I — Physics Engine & Station FSM
sim_server.py | rl_env/station_fsm.py
5 / 10
cruising
>
approaching
>
docking
>
stopped
>
doorsClosed
>
departing
Vehicle Phase State Machine
Physics Parameters
Tick Rate
20 Hz (50ms per step)
Physics motor frekansi
Max Speed
14 m/s (~50 km/h)
Metrobus hat limiti
Vehicle Length
20 m
Slot hesabi icin
Slot Size
25 m (20m bus + 5m gap)
Platform slot birimi
Comfort Braking
2.0 m/s^2
ETA hesabinda frenel ivmesi
Approach Zone
150 m before stop
Hiz duzenleyici aktif mesafe

## Slide 6
Implementation II — SmartStop Control Mathematics
rl_env/controller/smart_stop.py
6 / 10
Kinematic ETA (two-phase model)
Phase 1 (d > d_approach): ETA = (d - d_approach)/v + d_approach / (v_entry/2)
Phase 2 (d <= d_approach): ETA = d / (v_entry/2)
v_entry = min(v, sqrt(2 * a_c * d_approach)) [a_c = 2 m/s^2, d_approach = 150m]
Delay Budget
d_eff = d - v * 7.5s (computation 1s + comms 0.5s + driver 4s + vehicle 2s)
Intervention only if d_eff >= 30m
Cost-Benefit Decision
queue_time = t_ideal - ETA
cascade_cost = queue_time * N_follow * 0.7
downstream_cost = P_down * 8.0
net_benefit = cascade_cost + downstream_cost - queue_time
net_benefit > 0 --> SLOW DOWN
Speed Factor
lambda = clamp(v_needed / v_max, 0.3, 1.0)

## Slide 7
Implementation III — Coordination & System Results
rl_env/controller/stop_interface.py | Complexity Analysis
7 / 10
StopInterface — Decentralized Coordination
Downstream Pressure
P(s) = congestion(s+1)*1.0 + congestion(s+2)*0.6
Upstream Density
U(s) = density(s-1)*1.0 + density(s-2)*0.6
Mechanism
Shared state — each stop publishes, neighbors read (stigmergy)
Computational Complexity — Old vs New
Layer
Old Architecture
New Architecture
Improvement
Heavy ops/tick
N x S (~1,350)
S x 2 (~90)
~15x faster
Scalability
Grows with N
Fixed at S x 2
N-independent
Threading
Async scheduler
Single thread
No race cond.

## Slide 8
Challenges & Solutions
8 / 10
Physical Slot Access Constraint
Challenge: Vehicles enter from the rear — front empty slots are inaccessible
Solution:
rear_space = rearmost.position - bus_length - platform_tail - safe_gap rear_free = min(floor(rear_space / slot_size), capacity - occupied)
Delay Budget Timing
Challenge: Speed recommendation reaches driver after computation + comms + reaction delay
Solution:
d_eff = d - v * 7.5s Intervene only if d_eff >= 30m (ensures vehicle can still respond)
Slot Reservation Chain
Challenge: Multiple approaching vehicles must not target the same slot
Solution:
After each vehicle is processed, its assigned slot is updated in the timeline so the next vehicle sees the correct availability.
Oscillation / Hysteresis
Challenge: Small ETA fluctuations cause repeated on/off interventions
Solution:
Intervention threshold: eta >= ideal_arrival - 2.0s --> no action Prevents unnecessary speed adjustments near the boundary.

## Slide 9
Conclusion
9 / 10
Problem Reframed
Bus bunching is treated as a station slot overflow problem, not a headway deviation problem. This allows proactive intervention before bunching occurs.
Analytical Solution
The entire control system uses deterministic kinematic formulas. No machine learning, no training data, no black-box decisions.
Decentralized Architecture
Each SmartStop manages only ~1-2 vehicles in its zone. Complexity is O(S x 2) per tick regardless of fleet size.
Real-Time Performance
Physics engine runs at 20 Hz. Dashboard streams at 10 FPS via WebSocket. Full system runs single-threaded with asyncio.
Route Segment Testing
Dashboard allows selecting any sub-segment of the route for isolated testing. Vehicles spawn within bounds and wrap at segment end.

## Slide 10
Future Work
10 / 10
Cumulative Cascade Model
Current: cascade_cost = q * N * 0.7 Improved: cascade_cost = q * N*(N+1)/2 * 0.7 Each following vehicle carries the accumulated delay of all predecessors.
Upstream Density Integration
upstream_density is computed but not yet used in cost-benefit decisions. Incorporating it would allow preemptive slowdowns before a vehicle even enters a zone.
Adaptive Decay Weights
Downstream pressure uses fixed 0.6 decay. A speed-aware decay (based on actual ETA distances) would improve accuracy.
Multi-Route Coordination
Current system manages a single linear route. Extension to branching or intersecting corridors is an open problem.
Questions & Discussion