## Slide 1
Istanbul Metrobus
Analytical Station-Slot Control System
52 km
Corridor
45
Stations
800K+
Daily Passengers
20 Hz
Real-Time Physics
SmartStop · HeadwayModel · StopInterface · ControlMerger
1 / 10

## Slide 2
Problem Statement & Objectives
2 / 10
The Problem
• Vehicles cluster together (bus bunching)
• Large service gaps form on the route
• 800,000+ daily passengers affected
• Traditional headway control reacts too late
• One overflowed station cascades delays
Objectives
• Prevent station slot overflow
• Minimize cascade queue effects
• Real-time speed recommendations
• Purely analytical — no ML/RL
• Scalable: O(S×2) per tick

## Slide 3
Background & Motivation
3 / 10
52 km
Corridor Length
45
Stations
800K+
Daily Passengers
~2 min
Target Headway
Core Insight
Root Cause
Station slot overflow — not headway deviation
Old Approach
Measure headway gap → react with hold/skip → too late
New Approach
Predict slot availability → adjust speed before arriving
Key Property
Proactive control eliminates the need for reactive correction

## Slide 4
Design Methodology
4 / 10
Physics Engine 20 Hz
>
SmartStop x45 stops
>
StopInterface Coordination
>
ControlMerger Commands
>
Dashboard 10 FPS
Design Principles
Purely Analytical
Deterministic kinematic formulas — no ML, no training data
Decentralized
Each stop independently manages its own zone (~1-2 vehicles)
Single Thread
asyncio cooperative multitasking — simple, no race conditions
Forward Safety
Collision prevention layer always overrides speed commands

## Slide 5
Implementation I — Physics Engine & Station FSM
sim_server.py · rl_env/station_fsm.py
5 / 10
cruising
>
approaching
>
docking
>
stopped
>
doorsClosed
>
departing
Vehicle Phase State Machine
Physics Parameters
Tick Rate
10 Hz (100 ms/step)
Dashboard
10 FPS via WebSocket
Max Speed
25 m/s (~90 km/h)
Comfort Braking
3.5 m/s²
Slot Size
25 m (20m bus + 5m gap)
Approach Zone
150 m before stop
SmartStop Zone Logic
1. Each stop owns a zone [prev_stop → this_stop]
2. Filters only vehicles in its own zone (~1-2)
3. Computes ETA for each approaching vehicle
4. Checks slot timeline for earliest free slot
5. Runs cost-benefit: slow down or accept queue?
6. Publishes zone state to StopInterface

## Slide 6
Implementation II — Control Mathematics
rl_env/controller/smart_stop.py · station_arrival_scheduler.py
6 / 10
Kinematic ETA — Two-Phase Model
Delay Budget
Cost-Benefit Decision
Speed Factor

## Slide 7
Implementation III — Driver Speed-Band Advisory
rl_env/controller/control_merger.py
7 / 10
Advise a holdable BAND, not a point speed
A real driver cannot track "go 61 km/h, now 62, now 60" each second. We tell the driver "keep 60-70 km/h" — analogous to GLOSA speed advisory at traffic lights.
Anti-Chatter — 3 Layers
• EMA smoothing
needed speed low-pass filtered (tau = 2.5s)
• Min-hold
a band is kept at least 8s before re-issue
• Escape
re-issue early only on a real >8 km/h shift
Result
171 → 2
band changes per 60 s of simulation
No more per-second "speed up / slow down" flicker
Advisory Lifecycle
SLOW DOWN
early arrival risks slot overflow → band drops (e.g. 50-60)
>
HOLD
driver keeps the band; metering happens while cruising
>
RESUME
risk cleared → band climbs back to full speed (cue to speed up)

## Slide 8
Challenges & Solutions
8 / 10
Initial Approach: AI / Reinforcement Learning
The system was initially designed using a reinforcement learning agent to learn optimal speed policies. However, training instability, lack of interpretability, and the need for large amounts of simulation data made this approach impractical for a real-time transit control system.
-->
Switched to Analytical Control
Deterministic · Interpretable No training required
Delay Budget
Challenge: Speed command reaches driver ~7.5s after computation
Solution: d_eff = d - v × 7.5s | Skip if d_eff < 30m
Slot Reservation Chain
Challenge: Multiple vehicles may target the same free slot
Solution: Reserve each assigned slot immediately so the next vehicle sees updated availability
Physical Slot Access
Challenge: Front empty slots are unreachable — vehicles enter from rear
Solution: rear_free = floor(rear_space / slot_size)
Unrealistic Dwell Model
Challenge: A fixed dwell time per stop ignored real-world variability
Solution: Field-measured stochastic dwell: 15-30s, mean ~18s, shifted truncated-exponential (right-skewed)

## Slide 9
Conclusion
9 / 10
Problem Reframed
Bus bunching is a station slot overflow problem — not a headway problem. Proactive slot-based control prevents bunching before it occurs.
Analytical & Interpretable
Every decision follows deterministic kinematic formulas. No black-box models, no training, no data dependency.
Efficient by Design
O(S×2) heavy computations per tick regardless of fleet size. ~15× improvement over the previous architecture.
Real-Time Capable
Physics at 20 Hz, dashboard at 10 FPS. Single-threaded asyncio — simple deployment, no infrastructure needed.
Extensible
Route segment selection, slot timeline, downstream lookahead — all components are independently testable and replaceable.

## Slide 10
Future Work & Q&A
10 / 10
Passenger Density Metrics
The current system has no awareness of passenger load. Integrating real-time occupancy data — both inside vehicles and on station platforms — would enable demand-aware slot scheduling and more accurate dwell time estimation.
• In-vehicle load:
Adjust dwell time and slot priority based on passenger count
• Platform occupancy:
Detect crowded platforms early — trigger upstream slowdowns
• Demand prediction:
Historical patterns could improve ideal arrival time estimation
Cumulative Cascade Model
cascade_cost = q × N(N+1)/2 × 0.7 Each following vehicle carries accumulated delay — triangular sum is more accurate.
Higher-Fidelity Speed Formula
Today the GPS speed advisory already saves time via simple kinematics. A more realistic acceleration / comfort / traffic model would sharpen the band and the decision engine further.
Questions & Discussion