## Slide 1
Istanbul Metrobus
Analytical Station-Slot Control System
52 km
Corridor
45
Stations
800K+
Daily Passengers
Real-Time
Live Simulation
1 / 10
OĞULCAN ARAL
12120121
KHALED AL AKIDI
121200147
ARIF HUDDOGLU
120200074
SAVAŞ YILDIRIM
ADVISOR:

## Slide 2
Problem Statement & Objectives
2 / 10
The Problem
• Vehicles cluster together (bus bunching)
• Large service gaps form on the route
• 800,000+ daily passengers affected
• Traditional headway control reacts too late
• One overflowed station cascades delays
Objectives
• Prevent station slot overflow
• Minimize cascade queue effects
• Real-time speed recommendations
• Purely analytical — no ML/RL
• Scalable: O(S×2) per tick

## Slide 3
Background & Motivation
3 / 10
52 km
Corridor Length
45
Stations
800K+
Daily Passengers
~2 min
Target Headway
Core Insight
Root Cause
Station slot overflow — not headway deviation
Old Approach
Measure headway gap → react with hold/skip → too late
New Approach
Predict slot availability → adjust speed before arriving
Key Property
Proactive control eliminates the need for reactive correction

## Slide 4
Design Methodology
4 / 10
Physics Engine
>
Smart Stops x45
>
Stop Coordination
>
Speed Commands
>
Live Dashboard
Design Principles
Purely Analytical
Deterministic kinematic formulas — no ML, no training data
Decentralized
Each stop independently manages its own zone (~1-2 vehicles)
Single Thread
asyncio cooperative multitasking — simple, no race conditions
Forward Safety
Collision prevention layer always overrides speed commands

## Slide 5
How It Works I — Vehicle Movement & Stations
5 / 10
cruising
>
approaching
>
docking
>
stopped
>
doorsClosed
>
departing
Vehicle Phase State Machine
Realistic Movement
• Vehicles move with real-time physics
• Smooth, comfortable acceleration & braking
• Each vehicle safely follows the one ahead
• Stops have a limited number of platform slots
• Buses enter the platform from the rear
• Full buses form a queue outside the platform
SmartStop Zone Logic
1. Each stop owns a zone [prev_stop → this_stop]
2. Filters only vehicles in its own zone (~1-2)
3. Computes ETA for each approaching vehicle
4. Checks slot timeline for earliest free slot
5. Runs cost-benefit: slow down or accept queue?
6. Publishes zone state to StopInterface

## Slide 6
How It Works II — How a Stop Makes a Decision
6 / 10
1. Who is coming?
Each stop watches only the few vehicles inside its own zone.
2. When will a slot free up?
It estimates how long the buses now at the platform will stay.
3. Will this bus have to wait?
It predicts whether the bus arrives to a free slot — or to the back of a queue.
4. Is slowing down worth it?
It weighs the queue and the knock-on delays against a small slowdown.
5. Give the advice
If worthwhile, it suggests a speed so the bus arrives just as a slot opens — no stop-and-go.

## Slide 7
Driver Speed-Band Advisory
7 / 10
Advise a holdable BAND, not a point speed
A real driver cannot track "go 61 km/h, now 62, now 60" each second. We tell the driver "keep 60-70 km/h" — analogous to GLOSA speed advisory at traffic lights.
Why a Band, Not a Number
• Smoothing
ignores second-to-second noise in the target
• Hold
keeps a band steady instead of changing constantly
• Escape
updates early only when the situation truly changes
Result
171 → 2
band changes per 60 s of simulation
No more per-second "speed up / slow down" flicker
Advisory Lifecycle
SLOW DOWN
early arrival risks slot overflow → band drops (e.g. 50-60)
>
HOLD
driver keeps the band; metering happens while cruising
>
RESUME
risk cleared → band climbs back to full speed (cue to speed up)

## Slide 8
Challenges & Solutions
8 / 10
Initial Approach: AI / Reinforcement Learning
The system was initially designed using a reinforcement learning agent to learn optimal speed policies. However, training instability, lack of interpretability, and the need for large amounts of simulation data made this approach impractical for a real-time transit control system.
-->
Switched to Analytical Control
Deterministic · Interpretable No training required
Reaction Time
Challenge: A speed advice reaches the driver a few seconds later
Solution: We plan ahead for that delay before sending the advice
Slot Reservation Chain
Challenge: Several buses may aim for the same free slot
Solution: Each bus reserves its slot, so the next one sees it as taken
Physical Slot Access
Challenge: Empty front slots are unreachable — buses enter from the rear
Solution: We only count slots actually reachable from the back
Realistic Stop Times
Challenge: A fixed stop time ignored real-world variation
Solution: We use field-measured stop times that vary trip to trip

## Slide 9
Conclusion
9 / 10
Problem Reframed
Bus bunching is a station slot overflow problem — not a headway problem. Proactive slot-based control prevents bunching before it occurs.
Analytical & Interpretable
Every decision follows deterministic kinematic formulas. No black-box models, no training, no data dependency.
Efficient by Design
Work stays light even with a large fleet — each stop only looks at its own handful of vehicles.
Real-Time Capable
Runs live with a real-time dashboard, on a single machine — simple to deploy, no special infrastructure needed.
Extensible
Built from independent parts that can each be tested and improved on their own.

## Slide 10
Future Work & Q&A
10 / 10
Passenger Density Metrics
The current system has no awareness of passenger load. Integrating real-time occupancy data — both inside vehicles and on station platforms — would enable demand-aware slot scheduling and more accurate dwell time estimation.
• In-vehicle load:
Adjust dwell time and slot priority based on passenger count
• Platform occupancy:
Detect crowded platforms early — trigger upstream slowdowns
• Demand prediction:
Historical patterns could improve ideal arrival time estimation
Smarter Cascade Model
Account for delay that builds up across a whole chain of following buses — not just the next one — for more accurate decisions.
Higher-Fidelity Movement
A more realistic acceleration, comfort and traffic model would sharpen both the speed advice and the decision engine further.
Questions & Discussion